## Slide 1: Chapter 3: Communicating on a Local Network
Networking Essentials
Notes: Cisco Networking Academy Program
Networking Essentials
Chapter 3: Communicating on a Local Network

## Slide 2: Chapter 3 - Sections & Objectives
3.1 Principles of Communications
  Explain the importance of standards and protocols in network communications.
3.2 Talking the Language of Networking
  Explain how protocol model layers represent network functionality.
3.3 How do Ethernet Networks Work?
  Explain how communication occurs on Ethernet networks.
3.4 How are Networks Built?
  Explain why routers and switches are important in a network.
3.5 Routing Across Networks
  Configure devices on a LAN.
Notes: 2

## Slide 3: 3.1 Principles of Communications
Notes: Cisco Networking Academy Program
Networking Essentials
Chapter 3: Communicating on a Local Network

## Slide 4: Principles of Communications Establishing the Rules
The Three Elements
  The source, the destination, and the transmission medium.
Communication Protocols
  Before beginning to communicate with each other, we establish rules or agreements to govern the conversation.
Why Protocols Matter
  Networking protocols define the rules of communication over the local network.
Notes: 3.1 – Principles of Communications
3.1.1 – Establishing the Rules

## Slide 5: Principles of Communications So Who Makes the Rules
The Internet and Standards
  A standard is a set of rules that determines how something must be done.
  Networking protocols and Internet standards make it possible for different types of devices to communicate over the Internet.
Network Standards Organizations
  Standards are developed, published, and maintained by a variety of organizations.
Notes: 3.1 – Principles of Communications
3.1.2 – So Who Makes the Rules

## Slide 6: Principles of Communications Visualizing How Protocols Work
Stacking Them Up
  Successful communication requires interaction between protocols.
  A protocol stack is used to help separate the function of each protocol.
  This enables each layer in the stack to operate independently of others.
Using a Layered Model
  Layered models help us visualize how the various protocols work together to enable network communications
Notes: 3.1 – Principles of Communications
3.1.3 – Visualizing How Protocols Work

## Slide 7: Principles of Communications Visualizing How Protocols Work
Different types of Network Models
Protocol Model | Reference Model
TCP/IP Model | Open Systems Interconnection (OSI) Model
Notes: 3.1 – Principles of Communications
3.1.3 – Visualizing How Protocols Work

## Slide 8: 3.2 Talking the Language of Networking
Notes: Cisco Networking Academy Program
Networking Essentials
Chapter 3: Communicating on a Local Network

## Slide 9: Talking the Language of Networking Working with the OSI Model
Dividing the Tasks
  The OSI model divides communication into multiple processes.
    Each process is a small part of the larger task.
Notes: 3.2 – Talking the Language of Networking
3.2.1 – Working with the OSI Model

## Slide 10: Talking the Language of Networking Working with the OSI Model
Comparing the OSI and TCP/IP Models
  Both models are commonly used; therefore, it is wise to become very familiar with them.
Notes: 3.2 – Talking the Language of Networking
3.2.1 – Working with the OSI Model

## Slide 11: Talking the Language of Networking Protocols for Wired Networks
Why Ethernet?
  Ethernet has become the de facto standard
  This means it is used by almost all wired local area networks
Notes: 3.2 – Talking the Language of Networking
3.2.2 – Protocols for Wired Networks

## Slide 12: Talking the Language of Networking Protocols for Wired Networks
Ethernet is Constantly Evolving
  The Institute of Electrical and Electronic Engineers (IEEE) maintains Ethernet and wireless standards.
  They are responsible for maintaining the standards and for approving new enhancements.
Ethernet Addressing
  Each host connected to an Ethernet network is assigned a unique physical address which identifies it on the network.
  The physical address is known as the Media Access Control (MAC) address and is assigned to a NIC it when it is manufactured.
Notes: 3.2 – Talking the Language of Networking
3.2.2 – Protocols for Wired Networks

## Slide 13: 3.3 How do Ethernet Networks Work?
Notes: Cisco Networking Academy Program
Networking Essentials
Chapter 3: Communicating on a Local Network

## Slide 14: How do Ethernet Networks Work? Preparing Data for Transmission
Encapsulation
  The process of placing one message inside another message format is called encapsulation.
    De-encapsulation occurs when the process is reversed.
  Before a network message is sent over the network, it is encapsulated in a frame that identifies the destination and source MAC addresses.
Framing the Message
IEEE 802.3 Ethernet Frame |  |  |  |  |  | 
7 bytes | 1 | 6 | 6 | 2 | 46 to 1500 | 4
Preamble | Start of Frame Delimiter | Destination MAC Address | Source MAC Address | Type / Length | 802.2 Header and Data | Frame Check Sequence
Notes: 3.3 – How do Ethernet Networks Work?
3.3.1 – Preparing Data for Transmission

## Slide 15: How do Ethernet Networks Work? The Building Blocks of Ethernet Networks
Why Networks Need Hierarchical Design
  A MAC address identities a specific host on a local network, but it cannot be used to reach remote hosts networks.
  A hierarchical design is required.
The Benefits of Hierarchical Design
  Enterprise networks are most often designed in hierarchical manner using an access layer, distribution layer, and core layer.
  Hierarchical networks require a logical addressing scheme such as Internet Protocol version 4 (IPv4) or Internet Protocol version 6 (IPv6) to reach remote hosts.
Notes: 3.3 – How do Ethernet Networks Work?
3.3.2 – The Building Blocks of Ethernet Networks

## Slide 16: How do Ethernet Networks Work? Logical Addressing
Physical and Logical Addresses
  A MAC address is physically assigned to a NIC and never changes.
    The physical MAC address remains the same regardless of network.
  An IP address (network address) is logically assigned to a host NIC.
  The logical IP addresses contain two parts:
    Network portion: The left-hand portion of an IP address identifies the network portion of the address. It is the same for all hosts connected to the local network.
    Host address: The right-hand portion of an IP address that uniquely identifies the individual host on the network.
Both the physical MAC and logical IP addresses are required for a computer to communicate on a hierarchical network.
Notes: 3.3 – How do Ethernet Networks Work?
3.3.3 – Logical Addressing

## Slide 17: 3.4 How are Networks Built?
Notes: Cisco Networking Academy Program
Networking Essentials
Chapter 3: Communicating on a Local Network

## Slide 18: How are Networks Built? Starting with a Good Design
Access, Distribution and Core
Provides connections to hosts in a local Ethernet network.
Interconnects the smaller local networks.
Provides a high-speed connection between distribution layer devices
Notes: 3.4 – How are Networks Built?
3.4.1 – Starting with a Good Design

## Slide 19: How are Networks Built? Starting with a Good Design
Access Layer Devices
  Provides the first line of networking devices that connect hosts to the wired Ethernet network.
  Typically connected using Layer 2 switches.
Ethernet Hubs
  Legacy access layer device that broadcast frames to all ports.
  Created excessive collision domains.
  Hubs have been superseded by Layer 2 switches.
Notes: 3.4 – How are Networks Built?
3.4.1 – Starting with a Good Design

## Slide 20: How are Networks Built? Building a Better Access Layer
Ethernet Switches
  A switch accepts and decodes the frames to read the physical (MAC) address portion of the message.
  The switch checks a table on the switch, called a MAC address table, that contains a list of all of the active ports and the host MAC addresses that are attached to them.
  The switch creates a circuit that connects those two ports, enabling the switch to support multiple conversations between different pairs of ports.
Notes: 3.4 – How are Networks Built?
3.4.2 – Building a Better Access Layer

## Slide 21: How are Networks Built? Building a Better Access Layer
MAC Address Tables
Notes: 3.4 – How are Networks Built?
3.4.2 – Building a Better Access Layer

## Slide 22: How are Networks Built? Containing Broadcasts
What are Broadcasts Anyway?
  A broadcast message is simultaneously sent by a host to all other hosts.
  A broadcast MAC address in hexadecimal notation is FFFF.FFFF.FFFF
Broadcast Domains
  A local area network, a network with one or more Ethernet switches, is also referred to as a broadcast domain.
  When a broadcast message is sent, all switches forward the message to every connected host within the same local network.
Notes: 3.4 – How are Networks Built?
3.4.3 – Containing Broadcasts

## Slide 23: How are Networks Built? Containing Broadcasts
Communicating at the Access Layer
  To send a message, a host needs the IP address and MAC address of the destination host.
  The destination IP address is typically known; therefore, how does the sending host determine the destination MAC address?
  The sending host can use an IPv4 protocol called address resolution protocol (ARP) to discover the MAC address of any host on the same local network.
    IPv6 uses a similar method known as Neighbor Discovery.
Notes: 3.4 – How are Networks Built?
3.4.3 – Containing Broadcasts

## Slide 24: How are Networks Built? Containing Broadcasts
How ARP Works
Send data to a device
Is the MAC address in my ARP cache?
Receive ARP Reply from 10.1.1.1 with its MAC address
Send an ARP Request to IP 10.1.1.1
Send ping packet
No
Yes
  Dest MAC: FF-FF-FF-FF-FF-FF
The PC attempts to ping IP address 10.1.1.1.
PC> ping 10.1.1.1
The PC requires the destination IP address and MAC address.
Notes: 3.4 – How are Networks Built?
3.4.3 – Containing Broadcasts

## Slide 25: How are Networks Built? Distributing Messages to Other Devices
Dividing the Local Network
  As networks evolve, it is necessary to divide one access layer network into multiple access layer networks.
  There are many ways to divide networks based on different criteria.
Now We Need Routing
  Routers and routing is required to reach remote hosts.
  Routing is the process of identifying the best path to a destination.
Notes: 3.4 – How are Networks Built?
3.4.4 – Distributing Messages to Other Devices

## Slide 26: 3.5 Routing Across Networks
Notes: Cisco Networking Academy Program
Networking Essentials
Chapter 3: Communicating on a Local Network

## Slide 27: Routing Across Networks Keeping a Table
Selecting a Path
  Every router creates a routing table containing all locally-connected and remote networks and the interfaces that connect to them.
  Routers use their routing tables and forward packets to either a directly connected network containing the actual destination host, or to another router on the path to reach the destination host.
Building the Tables
  Router build their routing tables by first adding their locally connected networks, and then learning about other networks using routing protocols.
Notes: 3.5 – Routing Across Networks
3.5.1 – Keeping a Table

## Slide 28: Routing Across Networks Keeping a Table
How Routers Use Tables
  The router has added its two directly connected networks to the routing table.
Type | Network | Outgoing Port
C | 10.1.21.0/24 | FastEthernet 0/0
C | 172.16.1.0/24 | FastEthernet 0/1
Sending to Remote Networks
  If H1 sent a packet to H7, the router would examine its routing table and determine that to reach network 172.16.1.0/24 , it must forward the packet out of its Fa0/1 interface.
  Because the outgoing network is a directly connected Ethernet network, the router may also have to ARP the IP address.
Notes: 3.5 – Routing Across Networks
3.5.1 – Keeping a Table

## Slide 29: Routing Across Networks Creating a LAN
Local Area Networks
  Local Area Network (LAN) refers to a local network, or a group of interconnected local networks that are under the same administrative control.
  The term Intranet refers to a private LAN that belongs to an organization, and is accessible only by the organization's members, employees, or others with authorization.
Notes: 3.5 – Routing Across Networks
3.5.2 – Creating a LAN

## Slide 30: Routing Across Networks Creating a LAN
Assigning Hosts to a LAN
Notes: 3.5 – Routing Across Networks
3.5.2 – Creating a LAN