## Slide 1: Chapter 9: Testing and Troubleshooting
Networking Essentials 1.0
Notes: Cisco Networking Academy Program
Networking Essentials 1.0
Chapter 9: Testing and Troubleshooting

## Slide 2: Chapter 9 - Sections & Objectives
9.1 What to Do When It Does not Work
  Explain the steps to take when a new configuration does not work as expected.
9.2 Troubleshooting Issues in Networks
  Troubleshoot network problems with common network utilities.
9.3 Identifying and Fixing Common Problems
  Troubleshoot a network connectivity problem.
9.4 Working with Customer Support
  Explain how to work with customer support.
Notes: 2

## Slide 3: 9.1 What To Do When It Does Not Work
Notes: Cisco Networking Academy Program
Networking Essentials 1.0
Chapter 9: Testing and Troubleshooting

## Slide 4: What to Do When it Does not Work The Troubleshooting Process
What is Network Troubleshooting?
  Process of identifying, locating and correcting the problems.
  Maintain good documentation when troubleshooting.
Gathering Information
  Question the individual who reported
  the problem as well as any other
  affected users.
  Collect information about any
  equipment that may be affected
Notes: 9.1 – What to Do When it Does not Work
9.1.1 – The Troubleshooting Process

## Slide 5: What to Do When it Does not Work Approaches to Troubleshooting
  Choose a troubleshooting approach
  Top-down
  Divide-and conquer
  Bottom-up
Other Good Approaches
  Trial and Error
  Substitution
Notes: 9.1 – What to Do When it Does not Work
9.1.2 – Approaches to Troubleshooting

## Slide 6: 9.2 Troubleshooting Issues in Networks
Notes: Cisco Networking Academy Program
Networking Essentials 1.0
Chapter 9: Testing and Troubleshooting

## Slide 7: Troubleshooting Issues in Networks Detecting Physical Layer Problems
Using Your Senses
  Sight
  Smell
  Touch
  Hear
Using Software Tools
and Utilities
  ipconfig
  ping
  netstat
  tracert
  nslookup
Notes: 9.2 – Troubleshooting Issues in Networks
9.2.1 – Detecting Physical Layer Problems

## Slide 8: Troubleshooting Issues in Networks Troubleshooting Utilities
Windows IP Information
  ipconfig
  ipconfig /all
  ipconfig /release and ipconfig /renew
Notes: 9.2 – Troubleshooting Issues in Networks
9.2.2 – Troubleshooting Utilities

## Slide 9: Troubleshooting Issues in Networks Testing Network Connectivity
Using the ping Command
  Ping is used to test if a destination host is reachable.
  The ping command can be followed by either an IP address or the name of a destination host.
Notes: 9.2 – Troubleshooting Issues in Networks
9.2.3 – Testing Network Connectivity

## Slide 10: Troubleshooting Issues in Networks Testing Network Connectivity (Cont.)
What do ping Results Tell Us?
  If pings to both the name and IP address are successful, but the user is still unable to access the application, then the problem most likely resides in the application on the destination host
  If neither ping is successful, then network connectivity along the path to the destination is most likely the problem
  If the ping to the default gateway is successful, the problem is not local. If the ping to the default gateway fails, the problem resides on the local network.
  A ping may fail due to the firewall on the sending or receiving device, or a router along the path blocking the pings.
Notes: 9.2 – Troubleshooting Issues in Networks
9.2.3 – Testing Network Connectivity

## Slide 11: Troubleshooting Issues in Networks Other Useful IP Utilities
Can I Get to My Destination?
  The tracert utility provides connectivity information about the path a packet takes to reach the destination and about every router (hop) along the way.
Identifying Active Connections
  netstat lists the protocol in use, the local address and port number, the foreign address and port number, and the state of the connection.
Troubleshooting DNS
  The nslookup utility allows
  an end-user to look up information
  about a particular DNS name in
  the DNS server.
Notes: 9.2 – Troubleshooting Issues in Networks
9.2.4 – Other Useful IP Utilities

## Slide 12: 9.3 Identifying and Fixing Common Problems
Notes: Cisco Networking Academy Program
Networking Essentials 1.0
Chapter 9: Testing and Troubleshooting

## Slide 13: Identifying and Fixing Common Problems Connectivity Issues
Divide and Conquer
  Ping from a wireless client
  to the default gateway
  Ping from a wired client to
  the default gateway
  Ping from the wireless
  client to a wired client
Bottom Up
  Examine the LEDs
  LEDs may change color or
  flash to convey information.
Notes: 9.3 – Identifying and Fixing Common Problems
9.3.1 – Connectivity Issues

## Slide 14: Identifying and Fixing Common Problems How to Solve Common Issues
Cabling Problems
  Be sure to use the correct type of cable.
  Terminate cables via T568A or T568B termination standard.
  Do not exceed maximum cable run lengths.
  Verify that the correct ports are being used.
  Protect cables and connectors from physical damage.
Notes: 9.3 – Identifying and Fixing Common Problems
9.3.2 – How to Solve Common Issues

## Slide 15: Identifying and Fixing Common Problems Troubleshooting Wireless
Causes of Wireless Issues
  Not all wireless standards are compatible.
  Each wireless conversation must occur on a separate, non-overlapping channel.
  The strength of an RF signal decreases with distance.
  RF signals are susceptible to interference from outside sources
  APs share the available bandwidth between devices.
Authentication and Association Errors
  The SSID must match on both the AP and client.
  Both the client and the AP must be configured with the same authentication key.
  The same encryption key must be configured on both the AP and the client.
Notes: 9.3 – Identifying and Fixing Common Problems
9.3.3 – Troubleshooting Wireless

## Slide 16: Identifying and Fixing Common Problems DHCP and IP Address Issues
DHCP Server Configuration Errors
  The client table information should match the local host information
  Check to make sure that the router has an IP address
  The LAN interface of the wireless router should be set as the default gateway.
Notes: 9.3 – Identifying and Fixing Common Problems
9.3.4 - DHCP and IP Address Issues

## Slide 17: Identifying and Fixing Common Problems DHCP and IP Address Issues (Cont.)
Why Can’t We Get to the Internet?
  Examine the router status page.
  Check all physical connections and LED indicators.
  Try to re-establish connectivity
Could it be the Firewall?
  Check that the application
  TCP or UDP port is open
  and no filter lists are
  blocking traffic to that port.
  Check all settings on the
  router to ensure no
  security restrictions could
  be causing the issue.
Notes: 9.3 – Identifying and Fixing Common Problems
9.3.4 - DHCP and IP Address Issues

## Slide 18: 9.4 Working with Customer Support
Notes: Cisco Networking Academy Program
Networking Essentials 1.0
Chapter 9: Testing and Troubleshooting

## Slide 19: Working with Customer Support Using Outside Sources for Help
Where Can I Get Help?
  It might be necessary to obtain assistance from outside sources.
When to Call for Help
  It may be necessary to contact the vendor or ISP support desk for assistance.
Using the Support Desk
  It is important to give the support desk as much information as possible.
Notes: 9.4 - Working with Customer Support
9.4.1 - Using Outside Sources for Help

## Slide 20: Working with Customer Support Keeping Good Records
Resolving the Issue
  They may escalate the problem to a higher level.
  Record all information regarding the interaction with the support desk.
Tickets and Work Orders
  When the customer identifies
  who they are, the technician
  accesses the relevant customer
  information.
  The information is transferred to
  a trouble ticket, or incident report.
  When an on-site call is required,
  the trouble ticket information can
  be converted to a work order.
Notes: 9.4 - Working with Customer Support
9.4.2 – Keeping Good Records